## Slide 1: Wireless Communication via UART on a DE2Bot
Nisarg Himani
Sunny Patel
Thomas Saekao
Mohit Tandon
George Vellaringattu
ECE 2031 Digital Design Laboratory L05
Georgia Institute of Technology
April 23, 2014
1
Notes: Everyone

## Slide 2: Project Objectives
Implement serial communication using UART
Communicate between base station and robot
Modify the given program that allows UART to:
  Send messages to base station
  Receive jobs from base station
  Carry out jobs given by base station
  Return home
2
Notes: Nisarg

## Slide 3: Flow Chart of Communication
3
Notes: Sunny

## Slide 4: UART Interface
4
Notes: Mohit
UART Implementation
  Utilize DATA_STREAM_OUT_STB
  Allow the interface to be asserted where there is a valid byte of data.

## Slide 5: UART_DATA Interface
UART_STB comes from the UART interface
  Asserts with valid data
  Sets values for IO_DATA
I/O device verifies valid data without SCOMP
5
Notes: Mohit
UART_STB comes from the UART Interface and is asserted when the data in the UART is valid.
When UART_STB is asserted, IO_DATA is set to 0x0001.
When UART_STB is deasserted, IO_DATA is set to 0x0000.
Used to verify if the data is valid without modifying the SCOMP interface.
I/O Device
  A new I/O device was created to let the bot know when the DATA_STREAM_OUT_STB is asserted.
  Once it is asserted data can be collected.
  This I/O device prevents modifying the SCOMP.

## Slide 6: Movement Design
Two states
  Always facing out on the positive axes of the coordinate plane
  Moves backwards to drop off job
Odometry, x-axis then y-axis
Movement Efficiency
Consistency
Fast and Furious
6
Notes: George
Since we are only facing in the positive x- and y- direction, we don’t waste time rotating 180 degrees and face the negative x- and y- direction.
Together with movement efficiency and consistency, the bot moves quickly in the x- and y- direction and rotates quickly as well.

## Slide 7: Constant Movement Values
Variable | Value | Description
FMedium | 480 | Forward Speed
RMedium | -480 | Reverse Speed
TurnConst | 11 | Right Wheel Forward +11
TurnConst2 | 7 | Right Wheel Reverse -7
Deg90 | 113 | 90° anticlockwise
Deg270 | 456 | 270° anticlockwise
7
Notes: Thomas
We are rotating at a higher speed
Lower values for the degrees to allow for the momemtum of the bot and corrects for the rotation of the bot.
Q: Why CCW?
A: To keep it consistent, we kept everything consistent and easier to implement.

## Slide 8: Example Movement Layout
3. Dropoff coordinate (1,5)
- Move in y-direction
- Rotate 270° anticlockwise
- Move in -x direction
4. Go Home
- Rotate 90° anticlockwise
- Move in -y direction
- Pick up bot and realign it
1. Starting position (1,1)
2. Pickup coordinate (3,4)
- Move in x-direction
- Rotate 90° anticlockwise
- Move in y-direction
(1,1)
(3,4)
(3,1)
(3,5)
(1,5)
8
Notes: Sunny

## Slide 9: Problems Encountered
Polar coordinates
Accuracy in movement and rotation
Speed versus job time
Different odometry calibrations of DE2Bots
Inconsistent sonar
9
Notes: Nisarg
Accuracy in movement and rotation
  Having both wheels move at an equal speed resulted in the robot veering towards one direction
  The rotation angles were never a perfect 90 degree or 270 degree turn
  Going home ( staying within the blocks )
  Moving along legs versus moving along hypotenuse
  Sonar was very buggy

## Slide 10: Results
Failed turning 90° when going home after each job 1 time
Averaged 20 to 25 seconds per job
Completed all eight jobs in 225 seconds
Went out of the expected box 7 times
Picked up the bot 4 times
10
Notes: Mohit

## Slide 11: Discussion
Strengths:
  Fast movement and rotation speed
  Methodical movement
  Minimal waiting time
Weaknesses:
  Returns home after every job
  Only counterclockwise rotation
11
Notes: George

## Slide 12: Comparisons
12
Proposed Design
Actual Design
Notes: Thomas
Proposed
  Connecting output of UART interface to SCOMP
  Absolute movement based on current x,y position.
    Keep moving until required x,y position is reached
  Slow rotations
  Back to back jobs without going home
Actual
  Output of UART interface into i/o device
  Relative movement. Store x,y coordinate and move the required distance.
  Fast rotations
  Going home after each job to reduce error propagation
  Same
  Cartesian coordinates
  Odometry > sonar
  Fast movement for x,y directions

## Slide 13: Future Work: Polar Coordinates
Improving movement with the use of polar coordinates in terms of hypotenuse and theta values
(1,1)
(3,4)
(1,5)
1. Starting position (1,1)
2. Pickup coordinate (3,4)
- Rotate θ° anticlockwise
3. Dropoff coordinate (1,5)
- Rotate θ° anticlockwise
13
Notes: Thomas

## Slide 14: Future Work: Continuous Jobs
Being able to complete jobs one after another without the need to go home
Saving substantial amount of time to complete all eight jobs
14

## Slide 15: Reference Slides

## Slide 16: UART Pick-Up/Drop-Off Communication

## Slide 17: UART_STB Asserted/De-asserted Values